IO input and output (lighting control)

1. Requirements description:

JS:
H5 page initiates JS call, and initiates corresponding lighting control instructions according to the content status value in the page.

TCP:
APK receives server tcp command (EXTERNAL(150)), and initiates corresponding lighting control instructions according to the content status value.

2. Define protocol Define the following protocol for H5 call, TCP communication Control red Control blue Control green Control seven-color mixed flash Control light on Control light off Some reference materials

# 1. Set the color change of the LED light
adbcommand("echo w 0x04 > ./sys/devices/platform/led_con_h/zigbee_reset");
For example
0x04 is used to control red
0x05 is used to control blue
0x06 is used to control green
0x0b is used to control seven-color mixed flash
For details, please refer to the following code value table
https://www.showdoc.com.cn/server/api/attachment/visitFile?sign=4f6e581db9fb6cebd9cbc9e3457d1672&file=file.png
# 2. Control the brightness of the light:
----------------
0X00F7AA55
0X00F7XXXX
This is the standard NEC Code value, set the light display function
0X66RRGGBB
This is the customer-customized RGB function we added later
RR is red 0-255
GG is green 0-255
BB is blue 0-255
rk3288:/ # echo w 0x66550055 > ./sys/devices/platform/led_con_h/zigbee_reset
echo w 0x66550055 > /sys/devices/platform/led_con_h/zigbee_reset
rk3288:/ # echo w 0x66551155 > ./sys/devices/platform/led_con_h/zigbee_reset
echo w 0x66551155 > /sys/devices/platform/led_con_h/zigbee_reset

Can be operated directly by adb

resouces
https://www.showdoc.com.cn/electronictag/10504514092828682